The Purchaser shall provide Sound equipment that meets or exceeds the following criteria.

### FRONT OF HOUSE

Main sound reinforcement speakers must be of highest quality, appropriately powered and capable of producing 110dB over the frequency range of 50Hz to 17kHz with no audible distortion or extraneous noise, The show is not loud therefore the system must be “dead quiet”.  The system shall have sufficient number of speakers to cleanly disperse program to the entire audience area without extreme volume levels from any single speaker location.  The system crossover should be positioned at Front of House.  Preferred systems are flown line array systems where appropriate to the venue. EAW, vDosc, Vertec, Apogee, etc are all acceptable examples.

### CONSOLE

One Professional quality 24 channel mixing desk with a minimum of 4 auxiliary sends with switches from pre to post EQ, 4 sub groups, 4 band sweep equalization, and insert points on each channel and sub-group. The console must also be equipped with phantom power.  Preferred consoles are Soundcraft, Midas etc. Digital Consoles such as Digidesign Profile, Venue and Yamaha PM5d and M7CL are all acceptable.

ADDITIONAL PROCESSING 

                  	1 – Stereo Compressor/Limiter (BSS DPR901)

2 – Digital Reverbs (TC Electronics M-2000 or better)

1 – CD Player

4 – Stations of Clearcom (FOH audio, lighting director, monitor desk, stage manager)

### MONITORS

CONSOLE

One Professional quality 24 channel mixing desk with a minimum of 8 sends, 4 band sweep equalization, and insert points on each output. The board must also be equipped with phantom power.  Acceptable consoles are the Soundcraft MH2 or better.

6 – 31 Band graphic EQs

7 – High quality, LOW-PROFILE bi-amped wedges (EAW SM200iH preferred)                             no 15” or proprietary speakers permitted.

Adequate professional bi-amped power for all monitors

MICROPHONES

2 – Shure UHF-R /Beta 87 Wireless handheld microphone

1 – Shure UHF-R Dual Channel Wireless UHF Receiver

1 –Beta 87 handheld wired microphone

1 – DPA wireless Lapel mic system (for use on violin) + wireless belt pack option capability

4 – Shure Beta 58

1 – Sennheiser MD421

1 – Shure SM 57

1 – Shure SM 81 (with windscreen)

8 – Countryman Direct Boxes (confirm number of DI’s needed with Production Manager)

8 – Tall tripod Stands with Telescopic Booms

3 – Short tripod Stands with Telescopic Booms

1 – Straight Stand w/ ATLAS base

BACKLINE, etc

1 – Roland RD700 Keyboard. Also required is an adjustable piano bench and a ‘solid’ single keyboard stand as well as a sustain pedal and volume pedal.

3 – Guitar Stands

5 – Manhasset Music Stands with working stand lights (on dimmer please)

5 – Armless/Backless 30” high Bar stools

1 – 8’ x 12’ “Oriental or Persian style” carpet for use on stage

6 – Quad AC stage drops on the same power as audio for keyboard, pedals etc

QUESTIONS: 	Band configuration changes periodically, please confirm all details with

contact Mick Schmidtmeyer at 416-779-6230  mix-tour@rogers.com

LIGHTING:

These are the minimum lighting requirements.

Moving lights are not required

1 – Three colour overhead wash is required (Rosco 22, 17 & 80)

1 – Two colour front wash is required (Rosco 02 and 57)

10 – Front Specials

6 – Overhead Specials when possible

0 – Followspots.

Follow spots will not be used unless the show is in the round or on a rotating stage etc where using follow spots it is the only way to front light Mr. McDermott. In those cases diffusion will be required in the spots along with Rosco 34 and 02 colour

A basic lighting plot can be supplied if required.